## Slide 1: L700 Download User Guide (Flash loader v0.x Lite 7.0.2)
Jul. 2008 Suwon, Korea
S/W Platform2 Group
Mobile Communication Div.
SAMSUNG Electronics Co.. Ltd.

## Slide 2: Contents
Setting up configuration for L700 Downloader.
  How to install the USB driver.
  How to uninstall USB driver.
Usage of Downloader.
  Selection Binary.
  Checking main options.

## Slide 3: Setting up configuration(Install-1)
How to install USB Driver
  USB Driver\USBREGDRV-1.6
Click
Double
Click
Click
Click
Click

## Slide 4: Setting up configuration(Install-2)
  USB Driver\UPCDRIV-1.10.LMSQB10495_LMSQB15682\USB driver MCCI 4_38_9_330
Double
Click
Click
Click

## Slide 5: Setting up configuration(Install-3)
  How to install DFU device
    Invoke the Device Manager (Right-click My Computer then select Properties)
    Press “*-key + send-key” or “#-key + on-key”, then connect your phone with the usb cable (example : Y-cable).
    You can see new device, “USB Device with DFU Capabilities”.
    Right-click this device then click Driver Update.
    You have to select the file like “Flash loader v0.x Lite 7.0.2\52xdfu.sys” or folder like “Flash loader v0.3 Lite 7.0.2\” in the location of input box
  If you finished all usb driver installing, reboot computer.

## Slide 6: Setting up configuration(Uninstall-1)
How to uninstall USB Driver
  USB Driver\USBREGDRV-1.6
Double
Click
Select
remove
Click
Click

## Slide 7: Setting up configuration(Uninstall-2)
  USB Driver\UPCDRIV-1.10.LMSQB10495_LMSQB15682\USB driver MCCI 4_38_9_330
Double
Click
Click
Then, reboot your computer.
Click

## Slide 8: Usage of Downloader-1
Selection Binary
Click
Click

## Slide 9: Usage of Downloader-2
Checking main options
  1. NAND_FLASH as Location.
  2. Essential options for downloading:
  Erase, Exec, Write, Verify
  3. You must always select “Application size” as Erase Option.

## Slide 10: Usage of Downloader-3
How to start downloading
1. Enter the number of Device in small red box.
2. Press START button. Then, the text will change from “START” to “STOP”.
3. During you press keys(#+send-key, *+on-key), try to download by plugging in usb cable.

## Slide 11
THE END